## Slide 1
HP-75 S/W Development Prototype
Chuck McCord
Notes: This talk provides details of the HP-75 SW Development Prototypes

## Slide 2
Top View

## Slide 3
Front View

## Slide 4
Unit Label
Notes: This would indicate that at least 43 of these were in use the summer of 1982.

## Slide 5
Connected to HP75 with a Plug in module with standard springs and long module PCB
HP75 Plug-in Module
Notes: The HP75 modules were designed for a large number of insertions.
The clear module shows the gold spring structure.
The Dev system uses standard module plastic & springs with a large PCB for cable connection

## Slide 6
Uses standard HP 75 adapter
Unit Back view
Notes: The Development system uses the same AC adapter used by the HP75.

## Slide 7
HP 82059B
AC adapter

## Slide 8
It looks like a stock HP75C ….
… but it’s not …

## Slide 9
ESD test point
HP75 Back View

## Slide 10
HP75 bottom view
Notes: Another ESD test point.
The Development system HP75 has a RAM module and no Battery.

## Slide 11
Top View
After HP75 is removed

## Slide 12
Enlarged View

## Slide 13
Unit is built with 5 stacked stand-offs

## Slide 14
Back
Front
Notes: Stacked stand-offs in the 4 corners of the PCB and one at its center.
Unit’s thick sheet metal is very rugged- build like a tank.

## Slide 15
Bottom stand-off to elevate board above bottom case
Top stand-off to support top case

## Slide 16
Back
Front
Bottom
Top
Unit folded open
Notes: Top case unfolded from bottom.
2 power wires run from back panel to front of PCB
Power wires are long enough to stay connected with unit folded open

## Slide 17
Top Case
Notes: Power wires can also be disconnected

## Slide 18
Bottom Case
Front
Back
Notes: I have lots of pictures of the PCB to document this for others

## Slide 19
Front
Back
Enlarged view
of Full PCB

## Slide 20
Back
Front
Zooming in on back of PCB…
ZIF sockets for plug-in ROM Eproms and …
System ROM EPROMS in sockets–
the HP75 does not have ROMS inside
Notes: Zero-insertion sockets for plug-in ROMs easily accessible when unit is buttoned up.

## Slide 21
Back
Front
Notes: Front half of the PCB. Address decode logic and power supply.

## Slide 22
Back
Front
Notes: Close up of ICs & their part numbers

## Slide 23
Back
Front

## Slide 24
Notes: Notice all components are labeled on the PCB

## Slide 25: PCB IC Components
PCB label | HP Part # | Part Label | Look-up
U1 | 1820-1201 | Nat'l P144 | SN74LS08N
U2 | 1820-1197 | Nat'l P148 | SN74LSOON
U3 | 1820-1195 | 74ls175n | SN74LS175N
U4 | 1820-1199 | Nat'l P126 | SN74LSOhN
U5 | 1820-1430 | 74LS161AN | SN74LS161AN
U6 | 1820-1430 | 74LS161AN | SN74LS161AN
U7 | 1820-1430 | 74LS161AN | SN74LS161AN
U8 | 1820-1430 | 74LS161AN | SN74LS161AN
U9 | 1820-2215 | Nat'l B123 | MM74C373N
U10 | 1820-2215 | Nat'l B123 | MM74C373N
U11 | 1820-2215 | Nat'l B123 | MM74C373N
U12 | 1820-1208 | 74ls32pc | SN74LS32N
U13 | 1820-2053 | Nat'l B152 | DM74LS154N
U14 | 1820-2053 | Nat'l B152 | DM74LS154N
U15 | 1820-1201 | Nat'l P144 | SN74LS08N
U16 | 1820-1112 | MotI8125 | SN74LS74AN
U17 | 1820-1112 | MotI8125 | SN74LS74AN
U18 | 1820-1144 | MotI8130 | SN74LS02N
U19 | 1820-1207 | Nat'l I204 | SN74LS30N
U20 | 1820-1199 | Nat'l P126 | SN74LSOhN
PCB label | HP Part # | Part Label | Look-up
U21 | 1820-1197 | Nat'l P148 | SN74LSOON
U22 | 1820-1197 | Nat'l P148 | SN74LSOON
U23 | PROM | HN462532G | tms 2532jl-45
U24 | PROM | HN462532G | 
U25 | PROM | HN462532G | 
U26 | PROM | HN462532G | 
U27 | PROM | HN462532G | 
U28 | PROM | HN462532G | 
U29 | PROM | HN462532G | 
U30 | PROM | HN462532G | 
U31 | Prom socket |  | 
U32 | Prom socket |  | 
U33 | PROM | HN462532G | 
U34 | PROM | HN462532G | 
U35 | Prom socket |  | 
U36 | Prom socket |  | 
U37 | 1820-1144 | MotI8130 | SN74LS02N
U38 | 1820-1206 | 74ls27N | SN74LS27N
U39 | 1820-2215 | Nat'l B123 | MM74C373N
HP part number reference list:
http://hparchive.com/Bench_Briefs/HP-Bench-Briefs-1987-10-12.pdf
Notes: Complete IC Component List
No custom ICs!
You could build your own system. Module connector and PCB hardest parts to duplicate.
To decode the HP 1820- IC numbers I used reference….

## Slide 26: HP Part Cross Reference
Notes: This HP Bench Briefs issue has a very hand HP Part Cross reference to map from 1820- to commercial part number. This is on Eric’s archive drive.

## Slide 27
PCB
Back-side
Front
Notes: Back side of the 2 layer PCB.

## Slide 28
PCB Corrosion
Notes: This unit was stored in a garage and time was not kind. The PCB has corrosion in multiple places.

## Slide 29
PCB Corrosion

## Slide 30
PCB Corrosion

## Slide 31
PCB Corrosion

## Slide 32
PCB Corrosion

## Slide 33
PCB Corrosion

## Slide 34
PCB
Corrosion
Notes: So Far I have
Fiber cleaned traces
Reseated most of the socketed ICs
Multimeter checked adjacent traces- no shorts
Multimeter checked corroded traces- still have end to end continuity
Next steps will require a scope

## Slide 35
…. Similar …
Thank you!